## Slide 1: Advanced Control Methods
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: Advanced Control Methods
Limitations of classical control methods
Model Predictive Control (optimization-based)
Reinforcement Learning (learning-based)

## Slide 4: Why Go Beyond Classical Control?
Classical control methods: PID, linear state feedback (e.g., LQR)
Key limitations:
Limited scalability to complex systems: high-dimensional systems, coupled multivariable dynamics, time-varying behavior
Constraints not explicitly handled: actuator limits (saturation), safety constraints (position, temperature, pressure), rate limits typically handled after design (clipping, anti-windup)
Reliance on linear models: real systems often nonlinear, linearization only valid locally performance degrades away from operating point

## Slide 5: How to control systems when models are imperfect and constraints matter?
Examples:
Autonomous driving: constraints + planning
Robotics: nonlinear + coupled
Energy systems: large-scale + constrained
 Leads to two modern approaches:
Optimization-based control (e.g., model predictive control)
Learning-based control (e.g., reinforcement learning)

## Slide 6: Model Predictive Control (MPC)
Predict future system behavior using an explicit system model
Optimize control inputs over a finite horizon (control sequence)  choose best future trajectory

## Slide 7: MPC Optimization Problem
Minimize a cost function such as
Subject to constraints:
dynamics:
input limits:
state limits:
Terminal cost
Not restricted to linear dynamics + quadratic cost  can be any cost function reflecting the control objective

## Slide 8: Constraint Handling in MPC
Constraints are explicitly included in the optimization problem
 Only feasible control sequences are considered
Types of constraints:
Input constraints: actuator limits (e.g. max torque, saturation)
State constraints: position, temperature, pressure limits
Rate constraints: limits on how fast inputs can change

## Slide 9
Receding horizon principle: at each time step, apply only the first input of the chosen control sequence, then re-optimize at next time step
(future is uncertain, model is imperfect, disturbances occur)

## Slide 10: Intuition
MPC acts like a “smart planner”:
looks ahead into the future
chooses the best feasible trajectory
constantly updates the plan
MPC is like driving a car using a navigation system that constantly replans based on where you are.

## Slide 11: Contrast to Classical Control
PID / LQR:
Reactive
Fixed feedback law
Constraints: compute control, then clip if needed
MPC:
Predictive
Solves an optimization problem online
Compute control within constraints from the start
Car approaching a curve:
PID: “Too fast → brake hard (too late)”
MPC: “Will be too fast in 2 seconds → start braking now”

## Slide 12: Limitations of MPC
Requires an accurate model (model mismatch degrades performance, and modeling complex systems can be difficult)
Computational complexity (optimization problem solved at every time step  challenging for fast or high-dimensional systems)
What if the system is too complex to model accurately?
 Learn behavior directly from data

## Slide 13: Reinforcement Learning (RL)
Learning control from interaction  data-driven
Trial-and-error approach: no explicit model required
State: current situation of the system
Action: control input
Reward: measure of performance
Policy: mapping from state to action

## Slide 14: Reward Concept
Reward defines what “good behavior” means
Scalar signal received after each action (potentially also delayed effects)
Guides the learning process
RL aims to maximize long-term reward, e.g.,
Examples for reward: − tracking error, − energy consumption
Instead of telling the controller exactly what to do, tell it what is good or bad.
 Reward design

## Slide 15: Deep RL
tabular methods (calculating values for each state/action) simply memorize observed data
problem with tabular solution methods in practice: large state/action spaces (kind of curse of dimensionality)
 need for generalization: supervised learning to the rescue
non-linear function approximation over state/action space
nowadays often deep learning methods  Deep RL

## Slide 16: Contrast to MPC
MPC:
uses a known model
plans optimal actions
RL:
learns from interaction
discovers good actions over time
 RL replaces modeling with learning from experience

## Slide 17: Challenges of RL
Data inefficiency: requires large amounts of interaction data
Lack of guarantees: hard to ensure stability and constraint satisfaction
Computational complexity: training can be very expensive
Tuning and design choices: reward function, learning algorithm, exploration strategy have strong impact on performance
RL works well in simulation, but real systems are expensive and dangerous to experiment with (sim-to-real gap)

## Slide 18: Three Perspectives on Control
Classical:
PID, LQR
Simple, efficient, well understood
Limited for complex, constrained systems
 rule-based intelligence
Optimization-Based:
MPC
Handles constraints explicitly
Requires accurate system model
 model-based intelligence
Learning-Based:
RL
Learns directly from data
Challenges in safety and reliability
 data-driven intelligence
Modern control systems often combinations of the different ideas