## Slide 1: Systems
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: Systems
Static and dynamic behavior
Models
Proportional systems
First-order systems
Second-order systems
Linear Time-Invariant systems
Dead time

## Slide 4: Processes, Systems, Models
Process: the real-world phenomenon (physical, biological, ...), aka plant
System: abstraction of that process (behavior, dynamics)
Model: mathematical representation of the system
A system maps inputs to outputs (just like processes)
System
Input
Output
input: external force
output: displacement

## Slide 5: Static and Dynamic Systems
Static system:
Output depends only on the current input, no memory
Time-varying ≠ dynamic
Examples:
Resistor (model: )
Valve
Dynamic system:
Output depends on input and past states  evolves over time
Energy storage → memory
Examples:
Capacitor
Mass–spring–damper
(derivatives of )

## Slide 6: Examples from Electrical Engineering
input
input
output
output
model

## Slide 7: Mathematical Models
Algebraic equations (static systems)
Differential equations (dynamic systems)
Difference equations (discrete-time systems)
Define output separately:
…
input
output
state variable

## Slide 8: Differential-Equation Models
second-order system: energy storages mass and spring
(even if we choose , first-order only if we removed the spring)
Describe dynamics using derivatives
Example: mass–spring–damper system
Order of equation = system order
  = number of state variables
  = number of energy storage elements
Newton:
 Model:
(dissipation)

## Slide 9: Why We Need Models
Predict system behavior
Design controllers before implementation
Understand cause-and-effect relationships
Simplify complex real-world systems

## Slide 10: White-, Gray-, and Black-Box Models
 | White-Box | Gray-Box | Black-Box
System Knowledge | Full | Partial | None
Parameter Source | Physical | Mixed | Data Only
Interpretability | High | Medium | Low
Effort / Complexity | High | Medium | Low-Medium
Extrapolation | Reliable | Moderate | Poor

## Slide 11: Proportional (P) Systems
Output proportional to input
Static gain (gain = output divided by input), aka DC gain (zero frequency)
No dynamics
Examples:
  Amplifier
  Resistor:

## Slide 12: Integrating and Differentiating Behavior
Integrator:
  Accumulates input over time
  Introduces memory (energy storage)
Differentiator:
  Responds to rate of change
  Sensitive to fast variations
Physical systems often contain integrators and differentiators implicitly
 dynamic behavior (PT1, PT2, …)
dynamic

## Slide 13: Example: Free Fall
Velocity of a mass subject to a force:
Freefall:
Starting at with :
 grows linearly over time
Real-world: damping due to air resistance …
input
output
earth‘s acceleration (gravity)

## Slide 14: First-Order Systems (PT1)
One energy storage element ( 1)
Two system parameters:
Time constant  dynamic (T)
Static (DC) gain  proportional (P)
output–input ratio for a constant input after transients have died out, i.e.,
Step response:
A sudden change of the input signal to a new constant value, maintained thereafter:
63%

## Slide 15: Gain and Time Constant

## Slide 16: Solution for PT1 Differential Equation
Unforced (natural):
Forced:
Example:
At , step from to
Initial condition
Step response:
defined by initial conditions

## Slide 17: Derivation of Specific Example
Total response = forced (particular) response + natural (homogeneous) response
Particular response: constant input ()  constant solution
Determine from initial condition ()

## Slide 18: Free Fall with Viscous Damping
Account for air resistance:
 PT1 differential equation:
damping coefficient
Viscous damping is a simplified model.
In reality, aerodynamic drag is typically quadratic in velocity.
Linear damping is a good approximation for small velocities or near an operating point.

## Slide 19: Example: RC and RL Circuits
Transient responses to switching
Capacitor: Inductor:
But circuits without are not physically realizable (e.g., charging a capacitor would require infinite current)
 damping

## Slide 20: Transient Responses: RC Series Circuit
Differential equation:

Charging the capacitor with DC:
Transients: time-varying currents and voltages resulting from the sudden application of sources (usually due to switching)
Steady-state conditions with DC sources: capacitances behave as open circuits
system parameters

## Slide 21: Transient Responses: RC Series Circuit
Discharging the capacitor:
Differential equation:

## Slide 22: Transient Responses: RL Parallel Circuit


Steady-state conditions with DC sources: inductances behave as short circuits

## Slide 23: Second-Order Systems (PT2)
Two energy storage elements ( 2)
Three system parameters:
Natural frequency
Damping ratio
Static (DC) gain (as in PT1):
Different cases:
Underdamped ()
Critically damped ()
Overdamped ()
no oscillation
Step response:
can show oscillations
Series connection of two PT1:
Time constants determine behavior

## Slide 24: Solution for PT2 Differential Equation
Unforced (natural):
Forced:
Example:
At , step from to
Initial conditions ,
Step response:
with

## Slide 25: Derivation of Specific Example
Particular response: constant input ()  constant solution
Total response = forced (particular) response + natural (homogeneous) response
Determine and from initial conditions (, )

## Slide 26
Total response = forced (particular) response + natural (homogeneous) response
Determine and from initial conditions (, )
Total response = forced (particular) response + natural (homogeneous) response
Determine and from initial conditions (, )

## Slide 27: Example: Mass-Spring-Damper
At steady state:
without damping (
(for step input)
impulse:
same dynamics as step input

## Slide 28: Step and Impulse Response

## Slide 29: Example: RLC Series Circuit
, ,
Without : undamped
An circuit is a PT2 system whose step response is governed by natural frequency and damping, exactly like a mass–spring–damper system.
Frequency response (resonance) describes sinusoidal forcing. Here we focus on step response and transient behavior.
step voltage input
output: capacitor voltage

## Slide 30: Linear Time-Invariant (LTI) Systems
What do PT1 and PT2 have in common?
  Linear equations
  Constant parameters
  Superposition holds (scaling and additivity)
  Time shifts do not change behavior
 LTI systems
  Governed by linear differential equations
  Parameters do not depend on time
Foundation of classical control theory

## Slide 31: Dead Time
Time delay between input and output:
Common in processes and networks
  Transport phenomena
  Measurement delays
  Computation delays
Makes control more difficult
  Degrades stability margins
  Limits achievable performance

## Slide 32: Step Responses of Higher-Order Systems
The higher the order, the more the step response looks like a delayed step, even though there’s no actual dead time.

## Slide 33: Outlook: Frequency Response
So far, we tested systems with steps.
What if the input oscillates?
slow sinusoid → output follows
fast sinusoid → output attenuated / phase-shifted

## Slide 34: Summary: From Physics to Model
Identify inputs and outputs
Apply physical laws
Simplify assumptions
Validate against measurements