## Slide 1: Poles/Zeros & Stability
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: Poles/Zeros & Stability
Effect on transient response
Resonance
Frequency-domain stability analysis

## Slide 4: Poles and Zeros
Poles: roots of denominator
Zeros: roots of numerator
Determine system behavior

## Slide 5: Interpretation of Poles
System’s natural response:
sum of terms like (one term for each pole )
Real : purely exponential, no oscillation
Complex : (damped) oscillation
Single real pole: PT1
Two real poles: aperiodic PT2 (sum of two exponential terms)
Conjugate pole pair: oscillating PT2

## Slide 6: Pole Location
Pole real part determines decay/growth rate
, i.e., left half-plane (LHP): exponential decay  stable
, i.e., on imaginary axis: purely oscillatory  marginally stable
, i.e., right half-plane (RHP): exponential growth  unstable
Far to the left: fast decay
Closer to the imaginary axis: slower decay
Overall transient dominated by pole closest to imaginary axis

## Slide 7: Bounded Input Bounded Output (BIBO) Stability

## Slide 8: Stability of Continuous-Time Systems
Stable if all poles have negative real part
Marginally stable if poles on imaginary axis
Unstable otherwise
Stability checks for a known fixed transfer function of higher order:
Numerical solver for root finding: easiest and standard practice
Analytical alternatives without computing any roots, e.g., Hurwitz criterion (using determinants):
  Are there any RHP poles?
  Does stability change with a parameter? (root finding would require parameter scan)

## Slide 9: Zero Location
Zeros in LHP:
speed up response (derivative behavior)
can increase overshoot (caused by complex poles)
add phase lead (LHP poles have negative phase, so LHP zeros give the smallest possible phase lag  minimum-phase zeros)
Zeros in RHP:
cause inverse response (initial motion opposite to final steady-state direction)
add phase lag ( non-minimum-phase zeros)
Zeros at the origin introduce differentiating behavior
Zeros near poles modify or cancel dynamic modes
An LHP zero close to the imaginary axis or a zero close to a dominant pole (slowest-decaying exponential, i.e., pole with least negative real part) can increase overshoot significantly.
zero at :
inverse Laplace transform of :
zero at :
 
: (LHP pole: )

## Slide 10: Interpretation of Zeros
Zeros correspond to multiplications with  derivatives of the input
Describe how the input excites the natural modes (described by the poles)
Creates impulse-like behavior from step ()  faster initial rise
One can cancel a pole with a zero  corresponding exponential term of the pole disappears from the forced response
Amplification of higher frequencies ()
Frequency-selective property: system blocks steady-state sinusoidal response of complex frequency of a zero (despite nonzero input)
More zeros mean a stronger shaping of the input response and an increase of high-frequency gain.
Zeros alone do not make a system unstable, only poles in RHP do.

## Slide 11: Example: PT2 with LHP and RHP Zero
LHP zero: faster response, increased overshoot
RHP zero: inverse response (initial dip)

## Slide 12: Example: PT2 with LHP and RHP Zero
RHP zero closer to origin:
stronger dip
higher overshoot
more sluggish

## Slide 13: Example: PT2 with LHP and RHP Zero
Zeros increase high-frequency slope in the same way
LHP zero: phase lead +90°
RHP zero: phase lag -90°

## Slide 14: Pole-Zero Diagrams
Graphical representation in complex plane
Stability visible at a glance
Often calculated numerically
Example from last slides: both systems stable
(poles in LHP)

## Slide 15: Resonance
Large response at certain frequencies (if the system’s energy storage allows buildup)
 peaks in frequency response (Bode magnitude, sinusoidal response)
Due to lightly damped complex poles (natural modes)
Resonant frequency near imaginary part of the pole
For second-order system: (for small )
Mechanical systems often have very small damping  resonances dominate behavior
 Controllers must avoid exciting lightly damped poles

## Slide 17: Frequency-Domain Stability
Stability inferred from frequency response, i.e., examination of
Purely experimental approach, no mathematical model needed, no explicit pole calculation
Graphical instead of numerical methods: Nyquist curve, Bode plots
So far: open-loop analysis via Bode plots
Now consider closed-loop stability (feedback systems):
Given an open-loop transfer function, is the closed loop stable?

## Slide 18: Closed-Loop Stability
Given an open-loop transfer function , the closed-loop transfer function for negative feedback (with feedback path ) reads:
 For closed-loop poles:
Unstable if any solution for lies in RHP
loop gain
forward path
Typically, and a controller is included in the forward path:

## Slide 19: Nyquist Stability Criterion
Consider Nyquist curve for
 evaluation along the imaginary axis of (boundary of RHP)
Critical point : closed-loop pole
If curve encircles critical point, has solutions in RHP  closed loop unstable
(Encirclement is a topological signature of a root inside. It considers both positive-frequency and negative-frequency branches: )
Stable PT2 system:

## Slide 20
unstable

## Slide 21: Nyquist Formula
Number of encirclements  how many closed-loop poles in RHP
number of RHP poles of
number of closed-loop poles in RHP ( )
number of encirclements of by the Nyquist plot of , where the sign reflects the encirclement direction
 An unstable plant (e.g., ) can be stabilized by feedback (e.g., ).

## Slide 22: Gain and Phase Margins
Idea: measure distance to instability (of closed-loop system) from Bode plots
 practical robustness indicators
Instability:
In polar form:
If magnitude is less than at phase  stable
If magnitude is greater than at phase  unstable
Margins measure distance from that dangerous condition
Gain margin: how much the loop gain can be increased before instability
Phase margin: how much more phase lag can be tolerated before instability

## Slide 23: Crossover Frequencies
Phase crossover frequency:
Gain margin (unstable when <0):
Gain crossover frequency:
Phase margin (unstable when <0):
just barely stable:

## Slide 24
unstable: