## Slide 1: Continuous-time Controllers
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: Continuous-time Controllers
Control objectives
PID controllers
Working point
Proportional band

## Slide 4: Control
Models (differential equations) of dynamic systems allow to calculate the effect of inputs on outputs
Idea of control: modify the input in order to obtain a desired output
Example: adjust step input to reach a desired steady state ()
Problems: response may be too slow, disturbances degrade performance
PT1 system
PT2 system
Step responses

## Slide 5: Control Objectives
Stability (bounded output)
Fast response: rise and settling time
Low overshoot
Small steady-state error
Robustness (insensitivity to model uncertainty and disturbances)

## Slide 6: Control Loop
Feedback: measure system output, compare it to desired behavior (e.g., steady state), and use the resulting error as input to a controller
Goal: reduce error

## Slide 7: What Is a Controller?
System itself (subsystem of total control system), implemented in hardware or software
Input: measured error
Output: process input (low-energy control signal converted into physical action by actuator)
Hardware controllers
Fast, deterministic, limited flexibility
Examples: mechanical, analog electronic controllers using op-amps, FPGA-based (digital)
Software controllers (use of analog actuators via a digital-to-analog converter)
Flexible, complex algorithms, sampling delays (dead time)
Examples: Microcontroller-based, PLCs

## Slide 8: Example: Temperature Control
Sensor:
resistance thermometer to measure temperature (system output)
Controller:
digital electronic PID switching controller to activate the relay (controller output)
Actuator:
solid-state relay to switch a heater/cooler (plant) on or off

## Slide 9: On-Off Controller
Issue:
High-frequency switching stresses actuator
oscillations around setpoint
Example: industial oven
dead time
first-order process

## Slide 10: On-Off Controller with Hysteresis
Less switching at the expense of accuracy
On-off controllers are simple and low-cost, but have limited precision.
 Continous controllers (e.g., PID)

## Slide 11: PID Controllers
Most widely used industrial controller
  P
  PI: P + I
  PD: P + D
  PID: P + I + D
Example: pneumatic PID

## Slide 12: Proportional Control (P)
Control input proportional to error (static system):
Increases loop gain  faster response
Reduces damping  more oscillation
Steady-state error in many systems:
 settles at some error, just big enough to produce balancing the system dynamics (e.g., holding a mass up)
without controller
with P controller
overshoot

## Slide 13: Effect of Proportional Gain Parameter

## Slide 14: Historical: Centrifugal Governor in a Windmill
Working principle:
wind turns the blades
 blades turn a shaft (plant)
 shaft spins a pair of weighted arms (controller)
 arms mechanically twist the blades (actuator)
Automatic regulation:
faster rotation (controlled variable: angular speed)
 centrifugal force pushes weights outward (error: deviation from position at reference angular speed)
 blades are twisted to catch less wind (proportional control)  slower rotation
Steady-state error: need for twisted blades to balance torque from wind and load  speed offset

## Slide 15: Integral Control (I)
Integrator accumulating past error (dynamic)
Eliminates steady-state error to step inputs
Slower response
Reduces damping  more oscillation
Order of total system increases
PT1 → second order
PT2 → third order

## Slide 16: Derivative Control (D)
Derivative predicting future error based on the rate of change (dynamic)
Predictive action
Increases effective damping (keeps system near critical damping): less overshoot, fewer oscillations)
Derivative action amplifies high-frequency noise  often paired with a low-pass filter
Used less often in practice due to impact on system stability  PI

## Slide 17: PID Controller
Simple and intuitive
Works for many plants
Easy to tune experimentally
No model of process needed
 ~90% of industrial controllers are PID variants
P = speed
I = accuracy
D = damping

## Slide 18: Time-Domain Performance Trade-Offs
Faster response vs. stability:
Higher  faster response, but more overshoot and risk of instability
Accuracy vs. robustness:
Higher  higher accuracy, but more sensitive to disturbances
Damping vs. noise sensitivity:
Higher  less overshoot, but amplifies measurement noise

## Slide 19
Animated GIF

## Slide 20: Working Point and Linearization
Controllers designed and tuned around the operating/working point of the system
Linear approximation of nonlinear systems
Valid locally
W
W
Example: furnace

## Slide 21: Proportional Band
Range of error over which the controller moves its output (the input of the process to be controlled) from 0% to 100%
Inverse of proportional gain:
Smaller band  stronger control action (from 0% to 100% over a narrower error range)
Common industrial specification