## Slide 1: State Space Representation
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: State Space Representation
MIMO Systems
State variables and state equations
Controllability & Observability
State-space control
State estimation
Pole Placement
LQR
Kalman filter

## Slide 4: Multi-Input Multi-Output (MIMO) Systems
So far: single-input single-output (SISO) systems
Systems with multiple inputs and outputs (MIMO) become cumbersome to describe using transfer functions (focus on input–output behavior, limited insight into internal dynamics)
 Use of state-space representation (explicit representation of internal system dynamics)

## Slide 5: State Variables
State: minimal set of variables describing the system’s memory
 all information needed to predict future behavior
State variables define the system completely: given the current state and inputs, the future evolution is uniquely determined
Often correspond to physical quantities, e.g., position, velocity, current, voltage, temperature
Not unique: different choices of state variables can describe the same system
Input + Current State  Future State + Output
(instead of only relating input to output)

## Slide 6: State Equations
State equation (system dynamics):
Describes how the state evolves over time (time-domain formulation)
Output equation:
Describes how outputs are generated
Compact matrix form: naturally extends to MIMO systems
: state vector (internal system variables)
: input vector
: output vector
System matrices:
: system matrix (dynamics)
: input matrix
: output matrix
: feedthrough (direct input → output)

## Slide 7: Example: Mass-Spring-Damper System
Differential equation (Newton’s law):
Choice of state variables:
 position  velocity
State-space form:
Matrix representation:
Physical modeling
For the sake of simplicity, we will no longer use vector arrows.

## Slide 8: Physical Modeling or Construction
Two ways to get a state-space model:
From physics → define states → get matrices: physical states
From a transfer function → define matrices → get states: structured, useful for design (canonical forms)
 Same system, just different coordinates

## Slide 9: From Transfer Function to State Space
Transfer function describes input-output behavior in the Laplace domain:
For controllable canonical form:
From , obtain time-domain equation (via inverse Laplace transform)
Choose state variables based on derivatives of the output:
  , ,
Build state equations: Express highest derivative by lower-order states and input
Assemble into standard matrix form: ,
 Conversion of th-order differential equation into system of first-order equations

## Slide 10: Example: Second-Order System
, (not necessarily identical with the physical states)
,
,

## Slide 11: Controllable Canonical Form
Transfer function ⇄ State space
 same system, different representations
Also multiple valid state-space models (equivalent representations of the same system): choice depends on analysis or design goals
Canonical forms: designed system matrices (structured forms)
Controllable canonical form: input influences all states step by step
Example (second-order system, SISO):
, ,

## Slide 12: Observable Canonical Form
State-space representation constructed to give observable structure
Dual to controllable canonical form (transposed)
Example (second-order system, SISO):
, ,
 States for observable canonical form: ,
(typically not identical with the physical states)
Output directly depends on first state

## Slide 13: Controllability & Observability
Controllability: Can we move the system anywhere we want using the input?
Reaching all states via input signals
If a state is not controllable: no input can influence it  cannot be stabilized
Naturally emphasized in controllable canonical form
Observability: Can we figure out internal states from outputs?
Diagnosing a system through measurements (outputs)
If a state is not observable: it affects nothing we measure  hidden behavior
Naturally emphasized in observable canonical form
 A “good” system for control needs to be controllable + observable

## Slide 14: State Feedback Control
Core idea: control input based on full state
(use all internal variables for feedback)
Goal: shape system dynamics
 Faster response, improved stability, desired performance
Feedback gains:
For SISO is a row vector
For MIMO is a full matrix
Typically:
 Shift coordinates to stabilize at

## Slide 15: Pole Placement
Deterministic (manual) way to design state feedback :
Choose desired closed-loop pole locations explicitly
Compute such that eigenvalues of () match these locations
Requirement: system must be controllable
Direct control over dynamics
But no guidance on which poles are “best”

## Slide 16: Matrix Exponential
Insert into
 New system matrix of losed-loop system:
Solution of the system:
State transition matrix in form of matrix exponential (defined via power series): evolution of a vector of coupled states
Eigenvalues of this matrix () correspond to closed-loop poles
Poles of transfer function (no feedback):
 poles :

## Slide 17: Linear Quadratic Regulator (LQR)
For a linear system:
find a state feedback:
that minimizes the quadratic cost:
penalizes state deviation
penalizes control effort
Optimal control: automatically computes “best” feedback gains
Systematic design (no guesswork for poles)
Robust and widely used in engineering
Works naturally for MIMO systems
and chosen by the designer:
trade-off between performance and effort
In practice, using numerical solvers

## Slide 18: State Observers (State Estimation)
Issue: often not all state variables measurable
 Need to reconstruct state from output  observers
Observer dynamics:
Key concept: estimate
Requirements: system must be observable
Enables state feedback with limited sensors
observer gains
Output error: drives
Estimation error

 Observer pole placement

## Slide 19: Kalman Filter: Optimal State Estimation
Optimal observer for noisy systems
Handles measurement noise and process noise :
,
Same structure as general observer:
But chooses observer gain optimally by minimizing the estimation error (analogous to pole placement and LQR)
Widely used in practice: robotics, aerospace, navigation, finance

## Slide 20: Linear Quadratic Gaussian (LQG) Control
Combination of both ideas (modern control architecture):
Observer (estimation)   State Feedback (control)
Separation principle: controller design (LQR) and estimator design (Kalman) can be done independently
LQR: computes optimal control input
Kalman filter: estimates system state from noisy measurements

## Slide 21: Discrete-Time Note
Everything also exists in discrete time:
Example: predator-prey

## Slide 22: Key Takeaways
State space = internal system description
Enables MIMO + modern control
Controllability & observability are fundamental
State feedback + observers  full control
LQR & Kalman  optimal design