## Slide 1: Laplace Domain
Control Engineering

## Slide 2: Course Schedule
Systems
Continuous-time Controllers
Laplace Domain
Poles/Zeros & Stability
Controller Design
Discrete-time Controllers
State Space Representation
Advanced Control Methods

## Slide 3: Laplace Domain
Laplace transform
Transfer function
Frequency response
Bode plots
Bandwidth

## Slide 4: Why the Laplace Transform?
Converts differential equations (dynamic systems) into algebraic equations  easier to solve
Simplifies analysis and design
Natural language of control theory

## Slide 5: Reminder: Fourier Transform
Transformation from time to frequency domain:
Tells which frequencies are present in a signal or system
To be exact, tabulation of both magnitude and phase response at each frequency  complex numbers:
: how much of that frequency in the signal (how much the system scales each frequency)
: time shift of that frequency (how much the system shifts each frequency)

## Slide 6: Idea of Laplace Transform
Extend Fourier transform to include information about growth/decay behavior
 Add exponential weighting:
Combine frequency and growth/decay rate :
oscillation
growth/decay

## Slide 7: Definition of Laplace Transform
Integral transform from time to complex frequency :
Back transformation:

## Slide 8: Example
Laplace transform of :
Using partial integration:

## Slide 9: Laplace of Common Signals
Function | Time domain | Laplace domain
Unit Step |  | 
Delayed unit step |  | 
Unit impulse |  | 
Delayed unit impulse |  | 
Ramp |  | 
Exponential decay |  | 
Sine |  | 
Cosine |  | 
Function | Time domain | Laplace domain
Unit Step |  | 
Delayed unit step |  | 
Unit impulse |  | 
Delayed unit impulse |  | 
Ramp |  | 
Exponential decay |  | 
Sine |  | 
Cosine |  | 

## Slide 10: Properties of Laplace Transform
Linearity:
Convolution:
Derivative:
Integration:
Frequency Shifting:
Time Shifting:
Time Scaling:

## Slide 11: From Differential Equation to Transfer Function
Example: PT2 system
Time domain:
Frequency domain:
Transfer function: (assuming zero initial conditions)

## Slide 12: Transfer Function
Ratio of output to input in Laplace domain
Fully describes input–output dynamics of system, independent of input
In time domain, this corresponds to the convolution of the input with the impulse response of the system, assuming zero initial conditions:

## Slide 13: Transfer Function for PT1 System
Differential equation:
Laplace transform:
Transfer Function:
independent of input

## Slide 14: Example: Free Fall with Viscous Damping
where 

Transformation table:

## Slide 15: System Response with Transfer Function
Differential equation
(with
Solution
Algebraic equation
Solution
most elaborate part

## Slide 16: Transfer Function in Polynomial Form


roots of numerator: zeros
roots of denominator: poles
Input coupling:
describes how the input enters the system (can contain time derivatives)
Intrinsic system dynamics:
characteristic polynomial of the system
fundamental theorem of algebra
Causality requires (output cannot depend on derivative of input)

## Slide 17: Graphical Interpretation of Transfer Function
Contains (complex) poles and zeros
conjugate pair

## Slide 18: Poles and Zeros
Poles and zeros of a transfer function can be real or complex
Complex poles/zeros always appear in conjugate pairs for real physical systems (need for real coefficients in differential equations)
Poles determine stability and dynamics (system’s natural response)
,
Zeros shape the forced (input-driven) response
More about this later …
PT1: one pole
PT2: two poles

## Slide 19: Block Diagrams
Modular representation

## Slide 20: Block Diagram Algebra

## Slide 21: Series Connection
PT1
PT1
PT2
Example:

## Slide 22: Parallel Connection

## Slide 23: Feedback Connection
often unity

## Slide 24: Frequency Response
Response to sinusoidal inputs:
Amplitude and phase as function of frequency
Nyquist diagram:
Response = Transient part + Steady-state part

## Slide 25: Bode Plots
Magnitude (dB) vs frequency
Phase vs frequency
Logarithmic frequency axis
Example: PT1

## Slide 26: Bandwidth
Frequency range with good tracking (i.e., closed-loop system follows reference signal closely in shape, speed, and steady-state value)
Strong damping for higher frequencies (kind of filter on reference)
Typically consider frequency for which changes by : (amplitude drops to of its DC value)
Indicates speed of system: higher bandwidth → faster response
But also less robust and higher noise amplification
For amplitudes ():

## Slide 27: Individual Elements of Control Loops
Polynomial form of differential equation / transfer function:
 Transfer functions of individual elements by setting a portion of the coefficients to zero

## Slide 28: Proportional Element (P)
Consider :
or
(just constant gain)
Step response:

## Slide 29: Integral Element (I)
Consider , with :
or
(integrator gain or integral time constant)
Pole at
Step response:
Energy storage,
memory

## Slide 30: First-Order Lag Element (PT1)
Consider , with :
or
Step response:
Pole at

## Slide 31: PT1 Signal Flow Diagram
One energy storage

## Slide 32: Derivative Element (D)
Consider , with :
or
(differentiator/derivative gain or derivative time constant)
Amplifies high frequencies, i.e., noise
 use filtered differentiator (DT1)
Step response:
physically unrealizable  damping

## Slide 33: Filtered Differentiator (DT1)
Consider , with :
or
Step response:
 ideal D element
Used in PID controllers

## Slide 35: DT1 Signal Flow Diagram

## Slide 36: Second-Order Lag Element (PT2)
Consider , with :
Step response:
,

## Slide 37: PT2 as Product of Two PT1 Elements
can be written as product of two PT1 elements:
,
for real PT1 elements: (arithmetic-geometric mean inequality)
 overdamped () or critically damped () for
individual time constants
fastest non-oscillatory response

## Slide 39: PT2 Signal Flow Diagram
Two energy storages

## Slide 40: All-Pass Systems
Magnitude constant for all frequencies (), but phase depends on frequency
coefficients:
 Zeros are mirror images of the poles with respect to the imaginary axis.
Important in signal processing, e.g., for runtime alignment
first-order all-pass:
second-order all-pass:

## Slide 41: Systems with Dead Time
The transfer function of a system can be extended by multiplying it with the exponential term that represents a time delay:
Example: PT1 with dead time
Mainly suitable for frequency response analysis (e.g., Bode plots)
original transfer function
time delay (aka dead time)
Step response (P element with dead time):
TD

## Slide 42
Nyquist diagram for PT1 with dead time:
Nyquist diagram for system with dead time:
Bode diagram for system with dead time:

## Slide 43: Control Loop
closed-loop transfer function for negative feedback
above combines controller and plant

## Slide 44: PID Controller Transfer Function
: increases loop gain  faster response, smaller steady-state error, may increase overshoot
: adds integrator  eliminates steady-state error, may reduce stability margin
: adds damping  reduces overshoot, improves transient behavior
Controller design:
Shape the closed-loop poles to obtain the desired dynamics
Achieved by selecting and tuning controller parameters (move the closed-loop poles)

## Slide 45: Hidden Assumptions
reference prefilter: If reference shaping doesn’t affect stability, one can treat it separately.
sensor dynamics: If sensor is fast, one can assume unity feedback.
actuator dynamics: If actuator bandwidth ≫ closed-loop bandwidth, one can ignore it.
Always model what can affect poles

## Slide 46: Disturbances
Output as superposition of input and disturbances